## Slide 1: Progetto ISAF
Contesto Industriale e Obiettivi di progetto

## Slide 2: Boeing 787 - The Aerostructure Division’s role
Foggia
Horizontal
stabilizer
Grottaglie
Section 44
and 46
Nola
Machined parts fabrication
Pomigliano
Frame and shear ties fabrication

## Slide 3
First flight: 2009 / First delivery: 2011
787-8
242 passenger (two class configuration)
787-9
290 passenger (two class configuration)
787-10
330 passenger (two class configuration)
Key role in manufacturing the new generation pax aircraft.
Production of the horizontal stabilizer and the central and aft sections of the fuselage, which together total 14% of the aircraft’s structure.

## Slide 4
Sect. 46
Sect. 44
Leonardo Aerostructures Division
Single source in the production and assembly of S44 & S46 B787-8 / -9 / -10 and Horizontal Stabilizer of B787-8
Second source in the production of the Horizontal Stabilizer of B787-9 and B787-10.
Leonardo
Leonardo
Boeing

## Slide 5: Heritage – CFRP Fuselage Timeline
Boeing B787-8
1993
2007
2013
2016
Fuselage S44 & S46 One piece barrel
LDO OPB test
Boeing B787-9
Boeing B787-10
Fuselage S44 & S46 One piece barrel
Fuselage S44 & S46 One piece barrel
B787-S46
B787-S44
1990
McDonnell Douglas CAF
8 = 10058 mm (396”)
9/-10 = 13004 mm (512”)
8534 mm (336”)
2015
ATR OPB Demostrator

## Slide 6: Heritage – CFRP Wings Timeline
- Horizontal stabilizer
(cocured multispar)
Vertical Fin
(panels & cobonded stringers)
- Rudder & Elevator
- Wing mouv. Parts - Empennage mouv. parts
(H/C sandwich and full depth)
Vertical Fin
Horiz. Stabiliz. (cocured box)
- Wiing mouv. parts
- Horizontal stabilizer
(cocured multispar)
One Piece Barrel
(RFI frames)
AM-X
B767
B787
JSF
B777
- Wing
(Fiber placement panel)
- Wing panels (integral cobonded J-spar)
- Rear fuse panels
Eurofighter
- Horiz.Stabilizer (cocured multispar)
- Vertical Fin
(panels & cobonded stringers)
- Rudder & Elevator
ATR 42/72
- Outboard Flap (H/C sandwich 2nd generation)
- Barrier Walls
(large panels)
- Upper Beams
A380
1980 - 1995
1995-2020
C- Series

## Slide 7: ATR Program
ATR 42 / 72
Fin
Rudder
Stabilizer
Elevators

## Slide 8
Vertical Tail
Horizontal Stabilizer

## Slide 9: A220 Program
Bombardier St-Laurent
Cockpit, Rear Fuselage (TBC)
P&W
Geared TurboFan
C&D / Zodiac Interiors
SAC Center Fuselage,
Centre Wing Box, Doors
Bombardier Belfast
Wing
Rockwell Collins Avionics
Parker Hannifin Fuel & Hydraulics
Liebherr-Aerospace Toulouse Air Management System
Leonardo
Empennages

## Slide 10
Vertical Fin
Horizontal Stabilizer
On December 2008 Leonardo subscribed with Bombardier Aerospace a contract for the design, production and support of the Horizontal & Vertical Stabilizers for the CSeries models CS100 e CS300.
A220 Program

## Slide 11
Elevator
Center Box
Trailing Edge
Leading Edge
Tip
Visor Fairing
Multi-spar Box
6,13 m
3,45 m
1,30 m
Horizontal Stabilizer

## Slide 12
5,15 m
1,80 m
5,97 m
Rudder
Trailing Edge
Leading Edge
Tip
Dorsal Fairing
Torque Box
Vertical Stabilizer

## Slide 13
Block fully performed by Leonardo
Block partially performed by Leonardo
Cytec Material Quali to LDO Specification NTA
Leonardo Process Specification
Basic Allowables
ATR 42/72
Empennages
Boeing 787-8
Horizontal Stabilizer
Block fully performed by Leonardo
Block partially performed by Leonardo
Point Allowables
Elements
Process specification peculiarity
Airbus A220
Empennages
Block fully performed by Leonardo
Block partially performed by Leonardo
Cytec Material Qual to LDO Specification NTA
Basic Allowables
Process Specification NTA
© 2020 Leonardo S.p.a. All rights reserved.
This document contains information that is proprietary of Leonardo S.p.a. The information may not be used, disclosed, or reproduced without the prior written authorization of Leonardo.

## Slide 14: Assemblaggio ed installazione dello shim
ROOT RIB
SKIN PANEL

## Slide 15: Configurazione teorica
SHIM
Shim
Configurazione reale

## Slide 16: Motivazioni della variabilità
Tecnologia del composito
Dimensioni delle parti
Flessibilità delle parti
Condizioni di assemblaggio
Somma di tolleranze

## Slide 17
0.0125
(DIGITAL FEELER GAGE)
B
C
D
E
F
G
H
A
SHIM FOOTPRINT
Ad oggi il GAP viene misurato con un Filler Gage in diversi punti
A’
A
H’
H

## Slide 18
Il GAP differisce dal rilievo
I punti acquisiti vengono interpolate al fine di creare una superifcie
G’
F’
E’
B
C
E
F
B’
C’
D’
G
A’
H’
H
A
E’
B
C
D
E
B’
C’
D’
A’
H’
A
G’
G
F’
F
H
FLAT SIDE
D

## Slide 19
DELAM
DELAM
INADEQUATE SHIM
RESIDUAL GAP > 0.005”
Lo shim inadeguato produce, a lungo andare, una rottura a fatica delle parti

## Slide 20
Studio
Analisi variabilità
Studio degli stress degli shim
Misura
Studio di strumenti di misura
Studio dei processi di misura automatici
Soluzioni Tecnlogiche
Individuazione delle soluzioni
Dimostratore
Verifica delle soluzioni oggetto di studio
Benchmark
Sviluppo software
Studio dell’implementazione
Innalzamento di TRL su soluzioni particolarmente innovative
Calcolo predittivo dello shim
Obiettivi

## Slide 21
Studio
Analisi variabilità
Studio degli stress degli shim
Benchmark
Obiettivo 1 - Studio

## Slide 22
Obiettivo 2 - Misura

## Slide 23: Progetto ISAF
Soluzioni tecnologiche oggetto di studio

## Slide 24: Stato dell’arte del processo di shimming Materiale Sacrificale
Utilizzo di materiale sacrificale sulla parte in composito da fresare a controllo numerico
1. Bond GFRP sacrificial material on mating area
2. Machine sacrificial material on Rib
4. Machined sacrificial material on both surfaces ensure seamless installation
3. Machine sacrificial material on Panel

## Slide 25: Stato dell’arte del processo di shimming Shim Liquido
Uso dello shim liquido
1. Apply liquid shim on a part
2. Apply temporary load
4. Complete installation
3. Dry, check and clean

## Slide 26: Stato dell’arte del processo di shimming Shim in composito fresato
Il processo è iterativo e spesso porta a rilavorazioni
Gap measurement
Point interpolation
Shim CNC machining

< 0.005

> 0.005
Residual gap check
Shim installation

0.0125
0.0125

## Slide 27
Obiettivo 3 – Soluzioni Tecnologiche
Ottimizzazione del processo esistente
Sviluppo delle tecnologie di additive manufacturing sui materiali identificati come idonei per la produzione degli shim fuori scalo;
Sviluppo di tecniche di deposizione direttamente sulla parte (in-situ)
Realizzazione di attrezzature adattative con l’ausilio di tecniche di additive manufacturing

## Slide 28: Ottimizzazione processo esistente Shim in composito fresato
Il processo è automatizzato e non richiede iterazioni
Gap measurement
Point interpolation
Shim CNC machining

< 0.005

> 0.005
Residual gap check
Shim installation

0.0125
0.0125
Parts Measurement
Virtual Shim Simulator

## Slide 29: Stampa additiva shim
Il processo è totalmente automatizzato, non richiede iterazioni e utilizza Tecnologie e materiali innovativi
3D Print Shim
Shim installation
Parts Measurement
Virtual Shim Simulator
Shim stampato con tecnologia FDM in Carbon Peek

## Slide 30: Proprietà dei materiali e dei processi di stampa 3D
Una intensiva campagna di caratterizzazione dei materiali individuati (C-PEEK) per la realizzazione degli shim è stata condotta (Stampa 3D). Prove a trazione, compressione e tomografiche (per la distribuzione delle fibre) dei risultati del processo di stampa sono state condotte.
Esempi di provini a trazione realizzati
Esempi di analisi della distribuzione delle fibre per via tomografica

## Slide 31
Esempio di ispezione al SEM di un provino stampato in CPEEK
Analisi della frattura al SEM di un provino stampato in CPEEK

## Slide 32: Deposizione shim in-situ

## Slide 33: Realizzazione di attrezzature adattative